- Power down receiver

- Place one Jumper on J2 and on the Channel you want to extend the Pulse time

- Power up receiver.

- Receiver will provide 3 short beeps to inform of programming mode

- Press and hold any master button programmed onto selected Channel for approximaltely 3 seconds

- System will go into Settings mode.

1 flash = no latch, no panic

2 flash = Latch on, no panic

3 flash = Latch off, Panic on

4 flash = Latch on, Panic on

- Remove Jumper on J2 on first flash of LED and immediately fit Jumper again.

- Count flashes to adjust the Pulse time to your required time. 1 Flash = 1 Second

- Once required Pulse time flashed on LED remove Jumper

- Power down and remove J2  link